| Department of Electrical Engineering Technology Karakoram International University, Gilgit-Baltistan BOQ |
| --- |
| Electronics Lab |
| S.No | Name of Equipment/Device | Qty |
| 1 | Zener diode (5V, 12V,15V) | 500 |
| 2 | Capacitors (electrolytic, 10uF, 47uF,100uF, 1000uF) voltage ratings, 10V, 25V, 50V | 500 |
| 3 | LED Green + Red | 500 |
| Electrical Circuit Analysis Lab |
| S.No | Name of Equipment/Device | Qty |
| 1 | Electric circuit analysis trainer Specifications and features: Modular panel and rack/frame system facilitating alternate module locations and allowing for system expansion in the future Each component panel assembly must include: a 1/8" aluminum panel face; epoxy silk-screened component nomenclature and symbols; riveted, 16-gauge, formed-steel enclosures; powder coating and instructor fault switches Provision for mounting of system on standard DAC mounting structures, or any standard 19" rack system On-board circuit breaker, internal power supply, and transformer, creating working voltages of 24VAC center tapped, or 24VDC Dimensions (Minimum): (L x W x H) 18 1/8in. x 14in. x 17 1/2in. (460 x 355 x 444 mm) UTILITIES: 110/220 VAC, 50/60 Hz Accessories: Loose component kit including: (2) bar magnets, (1) component storage box, (1) magnetic reed switch, (1) nail, (1) spool of bell wire, (1) sealed box of iron filings, (1) D cell holder, (1) compass, (1) 6" acrylic rod, (1) rubbing cloth, (1) 6" wood dowel, (1) solderless breadboard (2" x 3"), (2) NPN transistors, (2) PNP Transistors, and (10) assorted resistors Banana plug patch cords Use/Activity Guide | 10 |

| 2 | Inductors (2.2uH,5uH,100uH, 220uH, 330uH, 470uH, 1mH, 4.7mH) | 500 |
| --- | --- | --- |
| 3 | Capacitors (electrolytic, 10uF, 22uF, 47uF, 100uF, 1000uF) voltage ratings: 10V, 25V, 50V | 500 |
| 4 | THREE PHASE BENCH POWER SUPPLY Specifications: Power Requirement: 240 / 415 VAC, 5Amp Single phase 50Hz Connection:3P+N+PE TECHNICAL SPECIFICATION: Three Phase AC Adjustable Output (0-240 / 415VAC; 1A With On / Off Switch, Overload Protection with Voltmeter and Ammeter Indicated) ACCESSORIES Operation Manual 1.5 M length input Cable and 3 pin plug. Dimensions: Approx. 470L x 360H x 250D | 5 |
| 5 | Three phase ac industrial connector (3 phase 4 wire) Specifications: TypeThree Phase Four Wire Power25A AC 440V SizeSocket: 88 x 80 x 45mm/ 3.4" x 3.1" x 1.8" (L*W*H) Plug: 75 x 67 x 27mm/3" x 2.6" x 1.1"(L*W*H) Fit for Cable Dia 15mm/0.6" Material Metal, Rubber | 6 |
| 6 | Connecting wires flexible cable 20A AC current (banana connector) Specifications: Power : 1000V, Connector Type : Banana Connector, Testing Pin Total Cable Length : 79cm / 31"/ 2.6Ft;Probe Length : 15mm /0.6";Probe Tip Dia. : 2mm / 0.1" 1 Pair (black+red) lead wires= 1 x threaded test probe tips,1 x Banana Connector | 2 |
| 7 | Stopwatch (Minimum 1 second) Specifications: Timing capacity: 9 hr, 59 min, 59 sec, 99/100 Resolution: 1/100 Countdown— Timing capacity: 99 hr, 59 min, 59 sec Resolution: 1 second | 10 |
| 8 | Breadboard (GL-12 830 Points) | 10 |
| 9 | Inductors (100uH, 50uH, 200uH) toroidal core | 500 |
| 10 | LED Green and Red | 370 |

| Applied Physics Lab |
| --- |
| S.No | Name of Equipment/Device | Qty |
| 1 | Capacitors (100uF, 220uF,1000uF) | 50 |
| 2 | Connecting wires (leads) banana connectors | 10 |
| 3 | Ballistics galvanometer Specifications: Resistance 100 Ω Time Period 12sec Charge Sensitivity 300mm/µC Current Sensitivity 1000mm/µA Critical Damping Resistance 2000 Ω | 7 |
| 4 | Simple pendulum consists of a brass bob of 1” diameter suspended by a flexible and weightless stitching thread the 2nd end of thread is tied to the rigid support. Supplied with heavy metallic base along with rod & special clamp | 5 |
| 5 | A standard capacitor 100uF 50v | 50 |
| 6 | A stopwatch (least count 1 sec) Specifications: Timing capacity: 9 hr, 59 min, 59 sec, 99/100 Resolution: 1/100 Countdown— Timing capacity: 99 hr, 59 min, 59 sec Resolution: 1 second | 10 |
| 7 | Keys for changing resistance on resistance box | 20 |
| 8 | Resistance box (1Ω, 10Ω, 100Ω, 220Ω, 330Ω, 1000Ω, 10000Ω) | 100 |
| 9 | Wooden box with moving lamp inside the box, photocell at one end of the box and with ammeter | 10 |
| 10 | Standard resistance box, Specifications: ±0.2% (Variable Decade Resistor 0-9999.9 Ohm) | 10 |
| 11 | Beaker (1000ml) | 3 |
| 12 | Thermometer digital NTC Specification: (-150 to 100 °C) +-1°C | 10 |
| 13 | 5 leads banana connector 1m | 5 |
| 14 | Universal Circuit Board Specifications: 9cm x 15 cm Double Sided FR4 Fiber Glass Dotted Veroboard | 10 |
| 15 | 150 Ohm Resistor 1/4W | 100 |

| 16 | 330 Ohm Resistor 1/4W | 100 |
| --- | --- | --- |
| 17 | 550 Ohm Resistor ¼ W | 100 |
| 18 | Miniature Light Bulb and Socket Specifications: 100W filament bulb with 1m cable and plug/socket pair | 10 |
| 19 | Jumper for breadboard | 10 |
| 20 | Wire Leads with alligator clips 1m | 100 |
| 21 | DC circuit trainer Specifications: Requires 220VAC to operate, outputs 2-14VDC (4A max) Panel mounted Digital Readout showing trainer DC voltage Hinged and removable top cover Built in DMM (Digital Multi-meter) display with accessible external meter fuse Meter is powered by the trainer’s power supply. (No batteries) Adjustable 2KHz pulse width modulation generator (0-100%) The following electrical components are included: Qty – component 2- #194 Light bulbs (removable) 1- #3157 Light bulb (removable) 1- #2726 LED bulb (removable) Buzzer Transistors (NPN and PNP) 1- Diode 1- Motor 1- ISO 5-pin relay 1- Electronic flasher 1- 75Ω Potentiometer 5- Resistors (1-2Ω, 2-20Ω, 1-40Ω, 1-100Ω) 1- Fuse (removable) 1- SPST Toggle switch 1- N.O. Push button switch | 10 |
| 22 | 1500 (17 AWG copper enamel wire 1 pound) | 1 |
| 23 | Two core cables (10A) | 1 |
| 24 | Ruler 12 inches | 10 |
| 25 | Bar magnets (colored blue and red on opposite poles) | 10 |
| 26 | Insulated copper wire Specifications: length = 10m, flexible AWG 3 | 1 |
| 27 | Empty Cardboard paper towel roll | 25 |

| 28 | Step Up Transformer Specifications: 12VAC /220VAC (1A) | 10 |
| --- | --- | --- |
| 29 | Step-Down Transformer Specifications: 220VAC/12VAC (1A) | 10 |
| Electrical Machines Lab |
| S.No | Name of Equipment/Device | Qty |
| 1 | Electrical Slide Rheostat Resistance 1.5A 50Ω | 9 |
| 2 | Connecting wires for trainers Specifications: (flexible with male banana connectors on both sides) | 20 |
| 3 | Current probes for oscilloscope Specifications: 10 Hz-2MHz Bandwidth Measurement 1mA to 1200A AC Low phase shift Diameter: φ52mm EN 61010, 600V CAT III High precision 0.1% | 10 |
| 4 | Voltage differential probes for oscilloscope Specifications: 50x/500x Bandwidth DC to 100 MHz (–3 dB) Attenuation ranges 10:1 / 100:1 DC accuracy ±2% Rise time 14 ns Input impedance 4 MΩ ∥ 5.5 pF each side to ground | 10 |

| 5 | 3 Phase AC Slip Ring Induction Motor Trainer Specification: Voltage: 415 V AC, 50 Hz Capacity: 300 W / 4 pole / 1500 RPM Rotor construction: Star connected, 4 terminals including star point brought out on 4 slip rings mounted on shaft Stator construction: 6 terminals are brought out to start the machine using star-delta starter Frame / mounting: 100 frames, chassis mounted Loading arrangement: Friction brake pulley for loading arrangement with 20 Kg spring balance for torque measurement Speed Measurement: Using hand held tachometer Control Panel Specifications: Aluminum profile modular flat table top demo panel carrying various high voltage components housed in plastic enclosures to minimize shock possibility Input 3 Phase DOL Starter Panel Integrated AC 3 Phase Multifunction Measurement Panel FWD-OFF-REV Switch Panel 3 Phase Wound Rotor and Synchronous Motor Panel DC Voltmeter and DC Ammeter Panel SCR Actuator (variable DC) cum sensor signal conditioning panel Instrumentation Power Supply cum Multichannel DPM Panel Hand Held Tachometer | 9 |
| --- | --- | --- |
| 6 | Eddy current brake Specifications: Type Air Cooled Eddy Current Brake Voltage 440V Finish Paint Coated Speed 500 RPM | 3 |
| 7 | Induction motor Specifications: HP 0.5, KW 0.37, V 200~220, Phase 1, A 3.5, RPM 1500, Hz 50 | 3 |
| 8 | Mimic panel | 3 |
| 9 | Three phase induction motor HP 1, KW 0.72, V 400~440, Phase 3, A~ 2, RPM 1500, Hz 50 | 3 |
| 10 | DC machine trainer Specifications: Should support following Characteristics and working principles of a DC Series motor Characteristics and working principles of a DC Shunt motor Characteristics and working principles of a DC Compound motor Characteristics and working principles of a DC Separately Excited motor Implementing correct wiring connections for DC motors electrical motor operation Measuring the voltage/current of electrical motor set Start/Stop motor control Motor speed measurement and testing | 10 |

| 11 | DC shunt generator Specifications: output Voltage: approx 220VDC Speed: approx. 1600 rpm Power: approx. 250W | 3 |
| --- | --- | --- |
| 12 | DC compound generator Specifications: output Voltage: approx 220VDC Speed: approx. 1600 rpm Power: approx. 100W | 3 |
| 13 | DC shunt motor Specifications: Input Voltage:220VDC Speed: approx. 1600 rpm Power: approx. 250W | 3 |
| 14 | DC compound motor Specifications: Input Voltage:220VDC Speed: approx. 1600 rpm Power: approx. 100W | 5 |
| 15 | Three phase transformer 2 kVA Specifications: Turn ratio: 1:1 Isolation type Provision to make star/delta connection on both primary and secondary side | 3 |
| Workshop Lab |
| S.No | Name of Equipment/Device | Qty |
| 1 | Pliers | 10 |
| 2 | Screwdrivers set (9 Pcs) | 10 |
| 3 | Tape measure | 10 |
| 4 | Electric tape | 100 |
| 5 | Paper tape for tagging | 100 |
| 6 | Wire stripper | 10 |
| 7 | Voltage tester | 10 |
| 8 | Wire crimpers | 10 |

| 9 | Splicing connectors | 100 |
| --- | --- | --- |
| 10 | Cable ties | 100 |
| 11 | Hammer | 5 |
| 12 | Handheld circuit finder Specifications: ACCURATE CIRCUIT BREAKER IDENTIFICATION (Quickly locate the correct breaker with precision using our circuit breaker finder, ensuring efficient electrical troubleshooting) TWO-PART SYSTEM (Consists of a Transmitter connected to the outlet/fixture and a Receiver to scan the panel, allowing for easy and accurate breaker identification) CLEAR INDICATIONS WIDE COMPATIBILITY (operating voltage 220 50Hz) BUILT-IN GFCI TESTER UNIVERSAL CONNECTIVITY (easy connection to pakistani grounded electrical outlets, ensuring seamless compatibility) | 5 |
| 13 | Insulated electric safety gloves | 100 |
| 14 | Safety glasses | 100 |
| 15 | FR4 pcb 6 *6 | 100 |
| 16 | pcb thermal transfer paper | 110 |
| 17 | Ferric chloride for pcb etching (5kg) | 1 |
| 18 | PVC tub for PCB etching | 7 |
| 19 | PCB CNC prototyping machine | 5 |
| 20 | PCB soldering stations | 10 |
| 21 | Electric cable 7/29 | 5 |
| 22 | Electric cable 3/29 Specifications: Strand Diameter .029 Inch Conductor Type Copper Insulation Type Poly Vinyl Chloride (PVC) | 5 |
| Control System Lab |
| S.No | Name of Equipment/Device | Qty |

| 1 | Ball and beam control module Specifications: The Ball and Beam module consists of a steel rod in parallel with a nickel-chromium, wire-wound resistor forming the track on which the metal ball is free to roll. The track is effectively a potentiometer, outputting a voltage that’s proportional to the position of the ball. When coupled to the Rotary Servo Base Unit, the tilt angle of the beam can be controlled by changing the servo gear angle. The Ball and Beam module can be operated in stand-alone mode, and the ball position can be controlled via the user interface plant = Rotary Servo Base Unit Ball and Beam module interface = USB Control Design environment = MATLAB(simulink) The license of MATLAB won’t be part of this, however Example codes + manual must be included | 10 |
| --- | --- | --- |
| 2 | QUBE Servo 2 or any other servo motor control trainer or Equivalent | 4 |
| Power System Lab |
| S.No | Name of Equipment/Device | Qty |
| 1 | Synchronization Trainer Technical Specifications: Sync trainer work in conjunction with Generation setup, HMI, RTU SCADA software and consists of following panels: Input 3 phase DOL Starter panel (1 Nos). 4 pole MCB of 415 V/20A. DOL 16A Contactor with 24DCV / 11VA COIL Bimetallic thermal O/L relay with range 9A - 15A RYB inputs indicators. 9 pin D (M) connector for SCADA interface. Manual start / stop with local trip contact Power ON LED indicator Synchronization Panel (1 Nos). Consisting of synchronization digital meter (Synchroscope), Manual Synchronization switch. 15W lamps X 6 nos.. Manual start / stop with local trip contact 3 Phase Bidirectional Power cum Energy meter panel (2 Nos). Bidirectional Multifunction 3 phase 3/4 wire, 415VAC, CT Input 5A LCD/LED display, Aux. supply 230V, 45-65Hz,5W Measure V. I., Hz, Pf, KVA, KW, KWH Modbus RTU RS 485 for SCADA | 5 |
|  | Mesh bus Generator panel (1 No). Consisting of 2-isolator switches, Circuit breaker, Generator bus, Grid bus, generator in feeder. 9 pin D (M) connector to interface with SCADA for automation. Manual start / stop with local trip contact. Power ON LED indicator Mesh bus Grid panel (1 No). Consisting of 2-isolator switches, Circuit breaker, Generator bus, Grid bus, Grid in feeder. 9 pin D (M) connector to interface with SCADA for automation. Manual start / stop with local trip contact. Power ON LED indicator Synchronization bus switch panel (1 No). Consisting of Circuit breaker, Main bus, Reserve bus. 9 pin D (M) connector to interface with SCADA for automation. Power ON LED indicator 415/110VAC, 50VA PT panel (2 No). Consisting of potential transformer, Input 415VAC, star connected, Output 110VAC, star connected, 50VA. Phase Angle meter panel (1 No). Measure phase angle between two voltages Internally 2 PTs for isolation. Modbus RTU RS 485 interface for SCADA. 37 pin D(M) to 9 pin D(F) converter panel (1 No). Consist of 37 pin D type male 1 no., 9 pin D type male 1 no. 9 pin D type female connectors 9 nos. Power ON LED. 5 pin to shrouded socket converter panel ( 2Nos). Consist of 5 pin 3 phase, 5 wires industrial female socket to connect 415VAC 3 phase supply. Shrouded banana sockets 18 nos to extend the 3 phase supply into individual setups. It’s used as bidirectional 3 phase extension board between two setups. Synchronization relay panel (1 No). Consist of automatic synchronization relay, Generator bus, Grid bus. 9 pin D (M) connector to interface with RTU/SCADA for automation. Aut Table top panels: Transmission line panel TL2 (1 No.) Consisting of 5 numbers of transmission lines. 2 Transmission lines of 0.3pu for 125Km. 2 Transmission lines of 0.2pu for 75Km. 1 Transmission line of 0.13pu for 50Km. R load Panel (1 No). 3 nos of 600W resistors with switch selectable 6 nos of taps at 100, 112, 150, 175, 200 & 225 ohm. Fault resistor 100ohm/600W. Multi pin heavy duty connector 32 pin & 24 pin to establish control from RTU/SCADA. Grid transformer Panel (1 No.) |  |

|  | 3 phase power transformer with connection group YY11, Input 415VAC, Output 415VAC, 5KVA, Secondary winding with tapping at ±2.5% and ±5%. Mechanical Dimension (mm) / Wt. (Kg): Rack: 1170(L) x 300(W) x 990(H) / Net Wt.: 65, Gross Wt.: 73 TL2: 600(L) x 385(W) x 500(H) / Net Wt.: 103 Load & fault panel: 600(L) x 275(W) x 500(H) / Net Wt.: 60 Grid X’mer: 770(L) x 275(W) x 435(H) / Net Wt.: 53 o/Manual switch Accessories: a) Tables for synchronization Setup: 1 no. consists of Pi type frame, Under trolley. Frame: 45X45 aluminum profile (Heavy duty) Colour: anodized white. Table top material/colour: The nova pan or Rubber wood with white/Silver gray with smooth finish veneer finish table top (18mm thick ) with removable central slot cover (900X500mm). Under Trolley: Located under individual setup table to house respective load panel, transmission line panel variac panel, transformer etc as applicable. Dimension: Table: 1450 mm (L) X 750 mm (W) X 760 mm (H). Under Trolley: 1200X700X185mm Caster wheels: Four sturdy castor wheels with locking mechanism are provided so that table can be positioned conveniently. b) Cables: i) 9 pin D male to 9 pin D female with 9 core cable, length = 0.450 to 6 meter – 6 nos. 37 pin D male to 37 pin D female patch cable, length = 4 meters – 1 no. RS485 patch cable: 6 pin mini DIN male to 6 pin mini DIN male, length 0.480 to 1.180 meter – 3 nos. List of experiments: Automatic as well as manual Synchronization of generator with grid supply. Study of V curve & inverted V curve. Study of Generator performance chart. |  |
| --- | --- | --- |
| 2 | Electrical Power Transmission Line Trainer Description: The functional modules of Trainer bench model equipment Artificial transmission line model. Generating TX model, Grid TX model. VAR Compensator & RLC loading model. Simulator instruments and protections scheme Input voltage min. 380V then step down in grid tx model is 300V Then step down by substation model in 250V And transfer voltage 220 to 250 volt to our locality. Transformer 300VA: 3EA Primary: 0/110/220/380V Secondary: 0 / 110 / 220 / 380V Resistive Load (5502, 1100 2, 1600 2 ±10%,200W) : 3 EA Inductive Load (1h,2h,3h, ±10%,): 3 EA Capacitive load (1.5uF,3uF,4.5uF, ±10%,): 3 EA | 5 |

|  | fan cooling system: 6 EA External AC connection facility The experimental studies with Equipment Ferranti effect – voltage profile of transmission under no-load condition ABCD Parameter Experiments Surge impudence loading, current at SIL Line loss and Line efficiency calculations Line voltage regulation studies Power handling capacity of the transmission line with different operating voltages Line VAR compensation and load VAR Compensation studies. Voltage improvement through tap changing Transformers studies. Accessory: Experimental Manual: 1copy; Connecting Cord: 1unit; |  |
| --- | --- | --- |
| 3 | Banana connector and plugs with wire | 200 |
| 4 | Measuring Instrument Trainer Scope of Learning Show skill in verification of Ohm’s Law. Verify the characteristics of series circuits. Verify the characteristics of parallel circuits. Verify the characteristics of mixed circuits. Show skill in measuring the power of an electric circuit. Show skill in grouping a number of cells to form a battery. Show skill in verifying kerchief’s Current law. Show skill in verifying kerchief’s Voltage law. Show skill in verifying Thevenin’s theorem. Show skill in verifying Norton’s theorem. Show skill in verifying Nodals’s theorem. Show skill in verifying Superpostion theorem. Show skill in verifying Maxwell theorem. Show skill in maximum power transfer theorem. Transformer Open Circuit Test Transformer Short Circuit Test Parallel Operation Of Transformer Regulation Test Of Transformer. Specifications: Digital Watt meter : 2 EA Analog AC Voltmeter : 3 EA Digital DC Voltmeter : 1 EA Digital AC Ammeter : 2 EA Digital DC Ammeter : 1 EA AC Power Supply (0~250VAC,50Hz) : 1 EA DC power supply unit (0,6,12,18,24,30,36V±10%,3 Amp) : 1 EA Resistive Load (550Ω, 1100 Ω, 1600 Ω ±10%,200W) : 3 EA Inductive Load (1h,2h,3h,±10%,) : 3 EA Capacitive load (1.5uF,3uF,4.5uF,±10%,) : 3 EA | 5 |

|  | fan cooling system : 6 EA Permanent magnet DC motor /Generator Set : 1EA 1 set DC generator Prime Mover : 1 EA External AC connection facility 1 Training Manual 4mm safety banana socket Size (L x W x H)= (60”x36”x12”) Weight: 60Kg (Approx) Power requirements: 220~240V AC, 50Hz Built-in short circuit protection system. |  |
| --- | --- | --- |
| 5 | Amplitude Modulation Work board 53-130 which comprises the following blocks: Signal Generation Modulation Filters Demodulation | 10 |
| 6 | Frequency modulation work board 53-140 which comprises the following blocks Signal generation Modulator Limiter Quadrative demodulator VCO Phase comparator | 10 |
| 7 | Module T20A for Pulse Amplitude Modulation | 10 |
| 8 | Feedback-Teknikit Console 92-300 | 10 |
| 9 | RJ-45 connector | 50 |
| 10 | Clamping Tool | 10 |
| 11 | Twisted Pair Cable (45 meter) | 2 |
| Instrumentation and Measurements Lab |
| S.No | Name of Equipment/Device | Qty |

| 1 | Transformer 230v/15v | 15 |
| --- | --- | --- |
| 2 | Bread board Specifications: GL-12 830 Points | 50 |
| 3 | Resistors ¼ W (1Ω, 10Ω, 100Ω, 220Ω, 330Ω, 470Ω, 1000Ω, 3.3kΩ ,10kΩ , 33kΩ ,100kΩ ,1MΩ) | 1000 |
| 4 | Variable Resistor (10k ohm POT with knob) | 100 |
| 5 | Inductors Specifications: (2.2uH,5uH,100uH, 220uH, 330uH, 470uH, 1mH, 4.7mH) | 100 |
| 7 | Lab trainer kit (Power supply 0- 30V 1A) + breadboard + DMM + screwdriver set) | 4 |
| 8 | Capacitors electrolytic, 10uF, 22uF, 47uF, 100uF, 1000uF 470uF | 100 |
| 9 | Resistance Box Specifications: (1,10,100,220,330,10k, 100k, 1M) ohm selection with keys option keys also included | 10 |
| 10 | LDR 10k | 100 |
| 11 | RTD | 10 |
| 12 | Ultrasonic Sensor Specifications: Arduino compatible | 15 |
| 13 | Energy Meter Specifications: Power = 0 to >-=10kW 230V/400V VAC communication interface Modbus or CAN bus over Rs485 Measurement parameters voltage current power power factor Mechanical properties can be installed on DIN rail should have a local lcd display | 10 |

| 14 | Electronic Wattmeter Specifications: power factor meter Power Meter Voltage (V) (10V~1000V, AC/DC, ±0.5%Udin) AC current (A) (upto 1000A, ±0.5%f.s.) Frequency (Hz) (40~70Hz ±50mHz) Power (W) (>15%S ±1%S) Power factor (0~1 ±0.02) Energy (Wh) (0~9999MWh ±1.5%rdg) Crest factor (1 to 10 ±5%) Features True RMS (Yes) Harmonic analysis (Up to 51th Yes) Flick measure (10 minutes, PST and PLT values Yes) Voltage ratio Yes Current ratio Yes Event capture Yes Trend capture Yes Data logging 8GB Yes USB interface Yes Backlight adjustment Yes Low battery indication Yes Input protection Yes power input 220VAC 50Hz battery backup supported | 3 |
| --- | --- | --- |
| 15 | Lux Meter Specicifications: Illuminance measurement (LUX): 0~199,900Lux Illuminance measurement (FC): 0~18,500Fc Accuracy: 0~9999Lux/0~999Fc: ±(4%+8), ≥10000Lux/≥1000Fc: ±(5%+10), ≥100000Lux/≥9999Fc: ±(5%+10) Resolution: 1Lux (0~9999Lux), 10Lux (≥10,000Lux), 100Lux (≥100,000Lux), 1Fc (0~9999Fc); FC=Lux/10.76, 10Fc (≥10,000Fc); FC=Lux/10.76 Sampling time: 0.5s Overload indication: OL MAX/MIN: Yes Data hold: Yes LCD backlight: Yes Auto power off: Yes Low battery indication: Yes Power: 1.5V battery (R03) x 3 LCD Display | 10 |
| Solar Energy Technology Lab |
| S.No | Name of Equipment/Device | Qty |

| 1 | Solar panel (180W) | 1 |
| --- | --- | --- |
| 2 | MPPT charge controller 20A | 1 |
| 3 | Battery (48AH) Specifications: Actual Voltage: 14.8V Nominal Capacity: 48AH Actual Capacity: >48AH Discharge Cut-Off: 12V Charge Cut-Off: 16.8V Charge Current: 15A Max Cont. Discharge: 15A Max Peak Discharge: 15A Max Charge Temperature: 32F to 110F Operation Temperature: -20F to 140F Charge Method: CC/CV Life Cycle: 800-1000 Terminal Type: Spade - F2 Connectors | 1 |
| 4 | Offgrid inverter 1kva | 1 |
| 5 | Ongrid inverter 3kva | 1 |
| 6 | Pyranometers GHI/DNI measurement Datalogging >=8GB or microSD card support battery backup, standalone, real-time clock | 1 |
| 7 | Solar path finder | 1 |
| 8 | Compass durable, rubber/ metal housing, | 3 |
| 9 | Angle finder ( inclinometer) | 1 |
| Wind Energy Technology Lab |
| S.No | Name of Equipment/Device | Qty |
| 1 | Wind turbine vertical (500W) PMSG Specifications: Rated Power 500W Rated Voltage 12V/24V/48 With Controller Yes Start Up Wind Speed 2m/s Rated Wind Speed 12m/s Survival Wind Speed 50m/s Wind Wheel Diameter/Height 0.65m/0.9m | 1 |

|  | Number of Blades 3 Blades Material Nylon Fuselage Material Aluminum alloy Magnetic Steel NdFeB Generator Type Three-phase AC permanent magnetically suspended generators Controller System Electromagnetic brakes Speed Regulation 360° Automatically Adjust Windard Installation Flange DN25 Degree of protection IP54 Gross Weight 21kg Top Net Weight 22kg Dimension 1060*270*490mm |  |
| --- | --- | --- |
| 2 | Wind turbine horizontal (500W)PMSG Specifications: Rated Power 500W Maximum Power 510W Rated Voltage 12V/24V/48V Start Up Wind Speed 2.5 m/s Rated Wind Speed 11 m/s Survival Wind Speed 45 m/s Wheel Diameter 1.75m Blase Number Nylon Fiber Generator Three Phase Permanent Magnet AC Generator Magnetic Steel NdFeB Generator Case Die-Casting Aluminum Controller System Electromahnet Speed Regulation Automatically Adjust Windard Installation Flange DN25 Working Temperature -40°C~80°C Package Dimensions 670*280*210mm | 1 |
| 3 | Wind speed logging setup (weather station) Specifications: Wind speed measurement (0 to 160kph) Wind direction measurement*0to 360 degree) Offline data logging Battery/charging supported Temperature logging Real time clock Rainfall | 1 |
| 4 | Charge controller for wind turbine 50A | 1 |
| 5 | Battery (48AH) Specifications: Actual Voltage: 14.8V Nominal Capacity: 48AH Actual Capacity: >48AH Discharge Cut-Off: 12V Charge Cut-Off: 16.8V Charge Current: 15A Max Cont. Discharge: 15A Max Peak Discharge: 15A Max Charge Temperature: 32F to 110F Operation Temperature: -20F to 140F Charge Method: CC/CV Life Cycle: 800-1000 Terminal Type: Spade - F2 Connectors | 1 |
| Robotics Lab |
| S.No | Name of Equipment/Device | Qty |
| 1 | 3D printer filament | 10 |

Dr. Bakhtiar Khan (HOD)	Engr. Saqib Shabbir (Lecturer)